Press Kit for

66th IAA Commercial Vehicles

Hanover 2016

Contents

- Hankook to become Original Equipment Manufacturer for Scania

- Hankook Supplies Original Equipment Tyres with 36 Sizes to MAN

- Hankook Tire Expands Original Fitment Supply Volume to Include Additional Sizes for Premium Trucks

- Hankook presents ultra fuel-efficient e-cube Blue long-haul tyre family

- Hankook SmartTouring: A new ultra-modern tyre for long-distance coaches

- Hankook SmartFlex AH35 and SmartFlex DH35: All-year truck tyres for regional traffic and winner of the Red Dot Award 2016

- Hankook SmartFlex AH31/DH3/TH31: All-rounders for all-year tyres

- Hankook AL10+ e-cube MAX: Low-line sizes for the steering axle

- Hankook SmartControl AW02: Winter tyres developed for truck steering axles and all other tyre positions

- Hankook SmartControl DW07: Winter specialist for the drive axle

- Hankook SmartControl TW01: New winter specialist for trailer tyres

- Hankook SmartWork range: Sturdy and durable for on and off-road

- Hankook TH22: Trailer tyres for low-bed truck transport

Hankook to become Original Equipment

Supplier for Scania

Tyre maker Hankook is to be the OE supplier for various Scania heavy-goods trucks and buses in the future. Scania, based in Södertälje in Sweden, is a part of Volkswagen Truck & Bus GmbH - one of the world’s leading manufacturers of trucks and buses for heavy transport applications. Scania is also leading provider of industrial and marine engines. Service-related products account for a growing proportion of the company’s operations, assuring Scania customers of cost-effective transport solutions and maximum uptime. Scania also offers financial services. From November 2016, Hankook will supply tyres to the production locations of the commercial vehicle manufacturer in Sweden. The equipment provided will include the truck tyre line e-cube MAX for long-haul traffic, as well as the SmartFlex, an all-year tyre for medium-haul applications suitable for the recently optimized Scania Euro 6 model among others. From 2017 onwards, the truck tyre line for construction site use SmartWork will also be added.

Hanover/Neu-Isenburg, Germany, 21 September, 2016 – Premium tyre maker Hankook is to be the Original Equipment Manufacturer to Scania, among others, in the future. Scania is part of the Volkswagen Group, one of Hankook’s largest OE customers world-wide. Hankook’s OE business with truck tyres for Scania will focus on Europe and will initially cover 18 dimensions in the 22.5 inch range. The new OE cooperation with Scania is Hankook’s second within the Volkswagen Group in the heavy commercial vehicles segment; Hankook has already been supplying various models within this segment to the MAN Truck & Bus GmbH since 2014.

“The cooperation with Scania in the original equipment segment is real proof of the quality of our products, since the e-cube MAX, SmartFlex and SmartWork lines were all able to meet the stringent specifications of the Scania engineers particularly in terms of performance, efficiency and sustainability,” says Ho-Youl Pae, COO for Europe at Hankook.

Plans include the equipment of all Scania truck and bus model ranges being produced in Europe. Tyres to be used include the e-cube MAX line for international long-haul traffic, a series which has been optimized for rolling resistance, and the new SmartFlex all-year tyre range, designed for flexible use between long-haul and delivery traffic. Construction site and offroad treads from the SmartWork series will also be introduced. Specially adapted for use on vehicles of the EURO 6 emissions class, the designated treads for the steering and drive axle score particularly well for environmental friendliness and service life – important aspects of TCO (Total Cost of Ownership) in the commercial vehicles OE business.

| Tread | Size | LI | Marking |  | M+S | Availability |
| --- | --- | --- | --- | --- | --- | --- |
| AL10+ | 315/80R22.5 | 156/150L (154/150M) | B/B/W1 70dB | - | - | ( |
|  | 315/70R22.5 | 156/150L | B/B/W1 70dB | - | - | ( |
|  | 315/60R22.5 | 154/148L | C/B/W1 70dB | - | - | ( |
| DL10+ | 315/80R22.5 | 156/150L (154/150M) | C/C/W1 73dB | ( | ( | ( |
|  | 315/70R22.5 | 154/150L | C/C/W1 73dB | ( | ( | ( |
|  | 315/60R22.5 | 152/148L | C/C/W1 73dB | ( | ( | ( |
| AL10 | 295/60R22.5 | 150/147K (149/146L) | C/C/W1 70dB | - | - | ( |
|  | 295/80R22.5 | 152/148M (154/149L) | C/C/W1 70dB | - | - | ( |
|  | 385/55R22.5 | 158L (160K) | B/C/W1 70dB | - | - | ( |
| DL10 | 295/80R22.5 | 152/148M | C/C/W2 75dB | - | ( | ( |
|  | 295/60R22.5 | 150/147K (149/146L) | D/C/W2 75dB | - | ( | ( |
| AH31 | 295/80R22.5 | 152/148M | C/B/W1 73dB | ( | ( | ( |
|  | 315/70R22.5 | 156/150L | C/B/W1 67dB | ( | ( | ( |
|  | 315/80R22.5 | 156/150L | C/B/W1 73dB | ( | ( | ( |
| DH31 | 295/80R22.5 | 152/148M | D/C/W2 75dB | ( | ( | ( |
|  | 315/80R22.5 | 156/150L | D/C/W2 75dB | ( | ( | ( |
|  | 315/70R22.5 | 154/150L | D/C/W2 75dB | ( | ( | ( |
| AH15 | 385/65R22.5 | 160K | C/B/W1 70dB | - | - | ( |

###

Hankook Supplies Original Equipment Tyres

with 36 Sizes to MAN

Tyre maker Hankook already supplies Original Equipment for various MAN long-haul trucks. At the 66th IAA for Commercial Vehicles in Hanover, the tyre maker will present 19 new dimensions in its Original Equipment portfolio for the bus and truck manufacturer. Among others, Hankook is supplying new sizes of its truck tyre ranges e-cube MAX, SmartFlex and SmartWork for various MAN models to the production facilities of the Munich-based manufacturer in Germany, Austria and Poland. The tyre ranges have been specially adapted for European conditions, boasting both ecological and economic advantages. The MAN Truck & Bus AG belongs to the Volkswagen Group, one of Hankook's largest OE customers worldwide. The OE business with Hankook truck tyres for MAN now covers a total of 36 dimensions in the 17.5, 19.5, 22.5 and 24 inch range.

Hanover/Neu-Isenburg, Germany, 21 September, 2016 – Premium tyre maker Hankook is already listed as an OE supplier for MAN with 36 dimensions. At the 66th IAA for Commercial Vehicles, the company will present 19 new dimensions of various Hankook truck tyre lines such as the e-cube MAX, SmartFlex and SmartWork series. The commercial vehicles specialist and the tyre maker have been cooperating since the first quarter of 2015. Ho-Youl Pae, Hankook COO for Europe comments: “The expansion of OE business in the commercial vehicles segment with MAN is of great strategic importance to us, as we can now offer further treads and dimensions for light to medium-duty trucks from MAN.”

The tyres will be fitted to the multi-award-winning MAN vehicle series TGX, TGS, TGM and TGL which are used for national and international long-haul, delivery and construction site traffic. Tyres used include the e-cube MAX line, which is tried-and-trusted for international long-haul traffic, the new SmartFlex all-year tyre range for flexible use between long-haul and delivery traffic, as well as construction site treads from the SmartWork series. Specially adapted for use on vehicles of the EURO 6 emission class, the treads – both as special steering and drive axle versions – score highly for environmental friendliness and mileage. This is also relevant to the TCO (Total Cost of Ownership), important for Original Equipment.

One special feature of Hankook's OE tyre portfolio for MAN are the new sizes in the low-line segment. With these, the premium tyre maker is demonstrating that its portfolio has already integrated the current market trend, namely the growing importance of low-line sizes in the truck business.

Hankook's range of Original Equipment tyres for MAN:

| Tread | Size | Model | LI | Marking |  | M+S | Availability |
| --- | --- | --- | --- | --- | --- | --- | --- |
| AL10+ | 315/80R22.5 | TGX | 156/150L (154/150M) | B/B/W1 70dB | - | - |  |
|  | 315/70R22.5 | TGX | 156/150L | B/B/W1 70dB | - | - |  |
|  | 315/60R22.5 | TGX | 154/148L | C/B/W1 70dB | - | - |  |
|  | 355/50R22.5 | TGX | 156L | C/B/W2 76dB | - | - | October 2016 |
| DL10+ | 315/80R22.5 | TGX | 156/150L (154/150M) | C/C/W2 75dB |  |  |  |
|  | 315/70R22.5 | TGX | 154/150L (152/148M) | C/C/W2 75dB |  |  |  |
|  | 315/60R22.5 | TGX | 152/148L | C/C/W2 75dB |  |  |  |
| AL10 | 295/60R22.5 | TGX | 150/147K (149/146L) | C/C/W1 70dB | - | - |  |
|  | 295/80R22.5 | TGX | 152/148M | C/C/W1 70dB | - | - |  |
|  | 385/55R22.5 | TGX | 158L (160K) | B/C/W1 70dB | - | - |  |
| DL10 | 295/80R22.5 | TGX | 152/148M | C/C/W2 75dB | - |  |  |
|  | 295/60R22.5 | TGX | 150/147K (149/146L) | D/C/W2 75dB | - |  |  |
| AH31 | 295/80R22.5 | TGM & TGS | 152/148M | C/B/W1 72dB |  |  |  |
|  | 315/70R22.5 | TGM & TGS | 156/150L | C/B/W2 73dB |  |  |  |
|  | 315/80R22.5 | TGM & TGS | 156/150L (154/150M) | C/B/W2 73dB |  |  |  |
|  | 385/65R22.5 | TGM & TGS | 160K | C/B/W1 69dB |  |  | October 2016 |
|  | 315/60R22.5 | TGM & TGS | 154L | C/B/W1 75dB |  |  | October 2016 |
| DH31 | 295/80R22.5 | TGM & TGS | 152/148M | D/C/W2 75dB |  |  |  |
|  | 315/80R22.5 | TGM & TGS | 156/150L (154/150M) | D/C/W2 75dB |  |  |  |
|  | 315/70R22.5 | TGM & TGS | 154/150L | D/C/W2 75dB |  |  |  |
|  | 315/60R22.5 | TGM & TGS | 154/148L (152/148L) | D/C/W2 75dB |  |  | October 2016 |
| AH11 | 215/75R17.5 | MAN TGL | 128/126M | D/C/W1 67dB | - | - | October 2016 |
|  | 235/75R17.5 | MAN TGL | 132/130M | D/C/W1 67dB | - | - | October 2016 |
|  | 265/70R19.5 | MAN TGL | 140/138M | C/C/W1 67dB | - | - | October 2016 |
|  | 285/70R19.5 | MAN TGL | 145/143M | C/B/W1 67dB | - | - | October 2016 |
| DH05+ | 215/75R17.5 | MAN TGL | 126/124M | D/C/W1 67dB | - |  | October 2016 |
|  | 235/75R17.5 | MAN TGL | 132/130M | E/B/W2 75dB | - |  | October 2016 |
|  | 265/70R19.5 | MAN TGL | 140/138M | D/B/W2 75dB | - |  | October 2016 |
|  | 285/70R19.5 | MAN TGL | 145/143M | D/C/W2 75dB | - |  | October 2016 |
| AM06 | 325/95R24 | MAN TGS | 162/160K | D/C/W2 72dB | - |  | October 2016 |
| DM06 | 325/95R24 | MAN TGS | 162/160K | D/C/W2 73dB | - |  | October 2016 |
| AM15+ | 385/65R22.5 | MAN TGS | 158L | D/C/W2 74dB | - |  | October 2016 |
| AM09 | 315/80R22.5 | MAN TGS | 156/150K | D/B/W1 67dB | - |  | October 2016 |
|  | 13R22.5 | MAN TGS | 156/150K | D/C/W1 68dB | - |  | October 2016 |
| DM09 | 315/80R22.5 | MAN TGS | 156/150K | D/B/W2 72dB | - |  | October 2016 |
|  | 13R22.5 | MAN TGS | 156/150K | D/C/W2 75dB | - |  | October 2016 |

###

Hankook Tire Expands Original Fitment Supply Volume to Include Additional Sizes for Premium Trucks

At the 66th IAA for Commercial Vehicles, Hankook is presenting its premium truck tyres from the e-cube MAX, SmartFlex and SmartWork series for the European market. These are now available in more than 42 sizes and are suitable for the complete Mercedes-Benz Actros and Atego model range. This means that Hankook has almost doubled its portfolio of dimensions for the original fitment of Daimler AG trucks since the cooperation started in 2014.

Hanover/Neu-Isenburg, Germany, 21 September, 2016 – Hankook further expands its original equipment (OE) portfolio in the heavy commercial vehicle (HCV) and medium duty segment as part of its existing OE agreements for Mercedes-Benz truck model range: Actros, Antos, Arocs, Axor, Econic and Atego. The tyre maker’s latest original equipment line-up includes among other the Hankook treads AL10+ e-cube MAX and DL10+ e-cube MAX, as well as the SmartFlex AH31 and SmartFlex DH31, all of which have been specially developed for the European market. Since the start of their original equipment business with Daimler AG, Hankook has expanded its portfolio for the Stuttgart-based truck and bus manufacturer to include more than 42 dimensions.

Hankook supplies multiple options for 22.5 inch tyres, the top-selling standard wheel size for heavy duty trucks in Europe, as well as for commercial vehicle tyres in the 17.5 and 19.5 inch sizes. Extending the OE fitment of the most-demanded heavy duty and medium duty trucks further strengthens the Hankook brand in a highly competitive market and is yet another milestone in the company’s endeavour for sustainable growth in the TBR business.

The e-cube MAX AL10+ (all position long haul) utilises linear grooves with waved walls to prevent uneven wear, enhancing durability and providing improved long-term fuel efficiency. The improved tread compound and high load index of the AL10+ increases fuel efficiency whilst simultaneously increasing load capacity. The e-cube MAX DL10+ (drive axle long haul) offers drivers excellent traction with three-dimensional kerfs and superior long mileage performance with extra-wide tread blocks and deep grooves. The block supporter also provides the DL10+ with boosted longevity and low rolling resistance. Both of these treads will be supplied in three sizes: 315/80R22.5, 315/70R22.5 and 315/60R22.5.

The SmartFlex AH31 is an all-season TBR tyre well-suited for variable road conditions, providing even wear and long mileage performance with significantly lower rolling resistance. The revolutionary drive axle tyre SmartFlex DH31 is perfectly matched for a number of different applications with its cutting-edge technology providing excellent traction in a number of different operating conditions. These include regional, long-haul and winter conditions due to the 3PMSF (Three Peak Mountain Snowflake), and also guarantee high mileage durability. The SmartFlex AH31 and SmartFlex DH31 will be available as original equipment in four sizes: 295/80R22.5, 315/60R22.5, 315/70R22.5 and 315/80R22.5.

In 2014, Hankook Tire was selected as an OE supplier for Mercedes-Benz medium duty ‘Atego’ trucks and the heavy duty model range ‘Actros’. Based on its position as a strategic partner for leading automakers like Mercedes-Benz, Hankook Tire has built a reputation for global top-tier technology and quality products in the TBR segments.

Hankook original equipment for Mercedes-Benz trucks:

| Tread | Size | Model | LI | Marking |  | M+S | Availability |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Smart Flex AH31 | 295/80R22.5 | Actros, Antos, Arocs, Axor and Econic | 152/148M (154/149L) | C/B/W1 72dB |  |  |  |
|  | 315/60R22.5 | Actros, Antos, Arocs, Axor and Econic | 160K(158L) | C/B/W1 70dB |  |  |  |
|  | 315/70R22.5 | Actros, Antos, Arocs, Axor and Econic | 156/150L | C/B/W2 73dB |  |  |  |
|  | 315/80R22.5 | Actros, Antos, Arocs, Axora and Econic | 156/150L (154/150M) | C/B/W2 73dB |  |  |  |
| Smart Flex DH31 | 295/80R22.5 | Actros, Antos, Arocs, Axor and Econic | 152/148M | D/C/W2 75dB |  |  |  |
|  | 315/80R22.5 | Actros, Antos, Arocs, Axor and Econic | 156/150L | D/C/W2 75dB |  |  |  |
|  | 315/60R22.5 | Actros, Antos, Arocs, Axor and Econic | 152/148 L | D/C/W2 75dB | - |  |  |
|  | 315/70R22.5 | Actros, Antos, Arocs, Axor and Econic | 154/150L | D/C/W2 75dB |  |  |  |
| AL10+ e-cube MAX | 315/80R22.5 | Actros, Antos, Arocs, Axor and Econic | 156/150L (154/150M) | B/B/W1 70dB | - | - |  |
|  | 315/70R22.5 | Actros, Antos, Arocs, Axor and Econic | 156/150L | B/B/W1 70dB | - | - |  |
|  | 315/60R22.5 | Actros, Antos, Arocs, Axor and Econic | 154/148L | C/B/W1 70dB | - | - |  |
| DL10+ e-cube MAX | 315/80R22.5 | Actros, Antos, Arocs, Axor and Econic | 156/150L (154/150M) | C/C/W1 73dB |  |  |  |
|  | 315/70R22.5 | Actros, Antos, Arocs, Axor and Econic | 154/150L | C/C/W1 73dB |  |  |  |
|  | 315/60R22.5 | Actros, Antos, Arocs, Axor and Econic | 152/148L | C/C/W1 73dB |  |  |  |
| AL 10 e-cube | 295/80R22.5 | Actros, Antos, Arocs, Axor and Econic | 152/148 (154/149L) | C/C/W1 70dB | - | - |  |
|  | 385/55R22.5 | Actros, Antos, Arocs, Axor and Econic | 158L (160J) | B/C/W1 70dB | - | - |  |
| DL 10 e-cube | 295/80R22.5 | Actros, Antos, Arocs, Axor and Econic | 152/148M | C/C/W2 75dB | - |  |  |
| AH15 | 385/65R22.5 | Actros, Antos, Arocs, Axor and Econic | 158L (160K) | C/B/W1 70dB | - | - |  |
| AH11 | 215/75R17.5 | Atego | 126/124M | D/C/W1 67dB | - | - |  |
|  | 235/75R17.5 | Atego | 136/134M | D/C/W1 67dB | - | - |  |
|  | 245/70R19.5 | Atego | 140/138M | C/C/W1 67dB | - | - |  |
|  | 285/70R19.5 | Atego | 145/143M | C/B/W1 67dB | - | - |  |
|  | 265/70R19.5 | Atego | 140/138M | C/C/W1 67dB | - | - |  |
| DH05+ | 215/75R17.5 | Atego | 126/124M | D/B/W1 70dB |  | - |  |
|  | 235/75R17.5 | Atego | 132/130M | D/B/W1 70dB |  | - |  |
|  | 245/70R17.5 | Atego | 136/134M | D/B/W1 70dB |  | - |  |
|  | 265/70R19.5 | Atego | 140/138M | E/B/W1 70dB |  | - |  |
|  | 285/70R19.5 | Atego | 145/143M | D/B/W1 70dB |  | - |  |
| AM06 | 10R22.5 | Atego | 144/142K | C/B/W2 72dB | - | - |  |
|  | 11R22.5 | Atego | 148/145K | D/B/W2 72dB | - | - |  |
|  | 12R22.5 | Actros, Arocs and Axor | 125/148K | D/C/W2 72dB | - | - |  |
|  | 13R22.5 | Actros, Arocs and Axor | 154/150K (156/150G) | D/C/W2 72dB | - | - |  |
|  | 315/80R22.5 | Actros Antos, Arocs, Axor and Econic | 156/150K | D/C/W1 72dB | - | - |  |
| TH22 | 215/75R17.5 | Actros (leading axle) | 135/133J | D/B/W1 70dB | - |  |  |
| SmartWork AM15 | 385/65R22.5 | Actros Antos, Arocs, Axor and Econic | 160K (160J) | D/C/W2 74dB | - |  |  |
| SmartWork AM15 | 275/70R22.5 | Atego | 148/145K | D/B/W2 74dB | - |  |  |
| DM03 | 315/80R22.5 | Actros Antos, Arocs, Axor and Econic | 154/150M (156L) | D/B/W2 76dB | - |  |  |
|  | 13R22.5 | Actros, Arocs and Axor | 154/150K | D/C/W2 76dB |  |  |  |
|  | 12R22.5 | Actros, Arocs and Axor | 152 / 148 K | D/C/W2 76dB | - |  | - |
|  | 11R22.5 | Atego | 148/145K | D/C/W2 76dB | - |  |  |
| AH22+ | 245/70R17.5 | Atego | 136/134M | D/C/W1 70dB | - | - |  |
| DH05W | 245/70R19.5 | Atego | 136/134M | D/C/W1 70dB | - |  |  |

###

Hankook presents ultra fuel-efficient e-cube Blue

long-haul tyre family

# Hankook has expanded its ultra-efficient and fuel-saving e-cube Blue trailer tyre line by special steering and drive axle treads. The tyre maker is exhibiting a complete solution for long-haul traffic which have A-label marking for rolling resistance on all axle positions for the first time at the 66th IAA Commercial Vehicle Show. The new tyre family is a long-haul system solution and stands out in particular on account of its ultra high fuel efficiency.

# Hanover/Neu-Isenburg, Germany, 21 September, 2016 – At the 66th IAA Commercial Vehicle Show, the premium tyre maker Hankook is presenting its complete ultra efficient fuel-saving truck tyre line for long haul duty called e-cube Blue. The already available trailer tyre e-cube Blue TL20 is teamed up now with new steering (e-cube Blue AL20) and drive axle (e-cube Blue DL20) treads and Hankook is thus exhibiting for the first time a complete solution for long-haul traffic which has A-label marking for rolling resistance on all axle positions. The new e-cube Blue line enables fleet customers to profit from an additional eight percent tyre related fuel efficiency and provides up to 55 percent more durability (less irregular wear, higher mileage) compared with current products.

# The tread design, which is tailored for each particular axle position also helps to further reduce fuel consumption and increase mileage without affecting dynamic characteristics such as braking and traction performance.

# Both central rib tread blocks of the e-cube Blue AL20 steering axle tyres support each other through their interlocking design, which increases tread block rigidity and helps to reduce rolling resistance. The stepped main tread groove design gives extra support for each tread block side. Moreover, they provide for excellent straight stability and good steering response. The largely closed tread design in the shoulder rib area ensures particularly uniform tyre wear.

# The tread appearance the e-cube Blue DL20 steering axle tyres is characterised by a central 4-block design of the massive central rib. The offset arrangement of the individual tread blocks guarantees interlocking action on both sides and results in mutual support for very good traction performance while reducing rolling resistance at the same time. In addition, the horizontally arranged semi-deep extra sipes in combination with tie bars in the open shoulder block area further promote traction.

# Moreover, the extra-wide contour of the e-cube Blue TL20 trailer tyres supports a very high driving stability and optimises wear resistance. The multi-sipes added in the central rib area prevent uneven wear without affecting tread rib stability. The closed 4-groove tread design guarantees excellent lateral stability and also a very low rolling noise.

# Common to all three e-cube Blue products is the newly developed tread compound with highly structured carbon black molecules for high fuel efficiency. In addition, the complete e-cube Blue tyre family also comprises all basic technologies of the successful Hankook e-cube product group, which uses amongst others Hankook's innovative mixture process IMS (Innovative Mixing System). This results in a particularly even distribution of carbon black and rubber molecules within the mixture. Together with longer mixing times at lower temperatures, this significantly increases the bonding rate between the carbon black and rubber molecules. As a result, e-cube tyres produce less heat during driving. The patented Hankook Stiffness Control Contour Theory (SCCT) design technology provides an even distribution of pressure inside the tyre and thus promotes more stability and less movement in the tyre. This results in high carcass durability and offers customers very good retreadability and economy.

###

Available dimensions of the e-cube Blue line

| Tread | Size | LI | Marking |  | M+S | Availability |
| --- | --- | --- | --- | --- | --- | --- |
| AL 20 | 385/55R22.5 | 160K | A/ CW1 72dB |  |  | In production |
| DL 20 | 315/70R22.5 | 154/150L | A/ CW1 72dB |  |  | In production |
| TL 20 | 385/55R22.5 | 160K | A/ BW1 66dB | - | - |  |
|  | 385/65R22.5 | 160K | A/ BW1 66dB | - | - |  |

Technical properties of the Hankook e-cube Blue tyre line

e-cube Blue AL 20: Steering axle tyres

e-cube Blue DL 20: Drive axle tyres

e-cube Blue TL 20: Trailer tyres

###

Hankook develops SmartTouring, a new

ultra-modern tyre for long-distance coaches

Tyre maker Hankook is launching a new coach tyre for long-distance travel in the European market. The company is anticipating that long-distance coach travel will grow in significance, and thus there will be an increasing demand for high-technology coach tyres. The new Hankook SmartTouring AL22 can be used on all axle positions and provides maximum ride and rolling comfort, excellent concentricity, a very low rolling noise and, as is customary with Hankook tyres, optimised rolling resistance and low wear for particularly efficient travel.

Hanover/Neu-Isenburg, Germany, 21 September, 2016 – Premium tyre maker Hankook is presenting a state-of-the-art tyre for long-distance European coach travel at this year's IAA for Commercial Vehicles. The Hankook SmartTouring AL22 will be available in the sizes 295/80R22.5 and 315/80R22.5 from market launch and is suitable for all long-distance coach wheels in all axle positions. Klaus Krause, Vice President and Head of the European Development Centre in Hanover adds: “During development of the SmartTyre line, we focused particularly on ride and rolling comfort as well as on a straight driving performance. The characteristics of the SmartTouring AL22 not only allow maximum travel comfort for passengers, they also maximise driving and handling comfort for the driver on long-distance trips.”

The carcass contour of the SmartTouring AL22 ensures the best suspension properties and contributes to a particularly safe driving style. The longitudinal 5-rib profile with its closed, solid central rib makes an excellent, straight driving performance possible at all times. Special Multi-3D sipes guarantee both good traction and an outstanding braking response.

The bead area of the SmartTouring AL22 has been developed for outstanding retreadability. In addition, its new contour achieves a particularly precise rim joint stiffness, which results in excellent concentricity and travel comfort.

The individual belt layers of the new SmartTouring AL22 are structurally arranged in such a way that significantly less heat is developed in operation compared to conventional tyres. This effect not only reduces rolling resistance, thus economising on fuel, it also considerably extends the service life of the tyre.

Fuel savings through reduced heat development have been achieved not only by the belt structure, but also by the tread compound used for the Hankook SmartTouring AL22. Special soot molecules with a larger volume and a particularly stable structure are used for the basic tread rubber, leading to a significant reduction in energy loss during movement. These so-called highly structured carbon molecules also guarantee enhanced abrasion resistance and, in combination with the other technologies, help to increase the mileage of the SmartTouring AL22 compared with conventional products by more than 17 percent.

Available dimensions of the SmartTouring AL22

| Tread | Size | LI | Marking |  | M+S | Availability |
| --- | --- | --- | --- | --- | --- | --- |
| AL22 | 295/80R22.5 | 154M | C/B/W1 71dB |  |  | In production |
|  | 315/80R22.5 | 156/150L | C/B/W1 71dB |  |  | In production |

Hankook SmartTouring AL22: Technical properties

Longitudinal tread profile with Multi-3D sipes and solid central rib

- High directional stability and comfortable handling response.

- Excellent straight driving.

- Very good braking and traction performance.

Special brake structure and newly developed bead area

- Reduced heat development.

- High retreadability.

New tyre compound with highly structured soot molecules:

- Low rolling resistance and reduced fuel consumption.

- Increased abrasion resistance, up to 17% increase in mileage

compared with conventional products.

###

Winner of the Red Dot Design Award 2016:

Hankook's all-year truck tyres SmartFlex AH35 and SmartFlex DH35 for regional traffic

Premium tyre maker Hankook is presenting the steering axle tyre SmartFlex AH35 and drive axle tyre SmartFlex DH35 for regional traffic for the European market. The all-year tyres, winners of the Red Dot Design Award in 2016, have particularly high traction on account of special Multi-3D sipes. In addition, the rigid tread blocks with minimum block movement promote fuel-efficient driving. Whilst SmartFlex AH35 made its debut at the Truck Grand Prix at the Nürburgring for German-speaking countries, the SmartFlex DH35 will be presented on the German Market on the IAA Commercial Vehicles for the first time.

Hanover/Neu-Isenburg, Germany, 21 September, 2016 – With the SmartFlex AH35 and SmartFlex DH35, fleets and forwarding agents benefit from a low-fuel, high-mileage and high-traction all-year tyre solution for the steering and drive axles. It is also possible to fit SmartFlex AH35 to all axles. In 2016, they were presented with the Red Dot Design Award. With these models, Hankook is extending the SmartFlex tyre line. Whilst the SmartFlex AH31 and SmartFlex DH31 are intended mainly for larger wheel sizes such as 22.5 inch, the SmartFlex AH35 and its counterpart SmartFlex DH35 for the drive axle are designated to the smaller 17.5/19.5 inch sizes.

The Multi-3D sipes anchored in the tread of the SmartFlex AH35 guarantee outstanding traction. The mixture of straight and wave-shaped grooves improves water drainage and prevents hydroplaning long-term. Without losing sight of the summer properties, the M+S marking and the 3PMFS symbol (snowflake) indicate that the tyre is also perfectly equipped for all wintry weather conditions such as slush, ice and snow. The rigidity of the tread blocks promotes particularly fuel-efficient driving. Equally, the special tread design supports even tyre wear so that the Total Cost of Ownership for fleet and forwarding agent companies can be reduced long term in terms of service life. The high mileage and performance of the tyre are guaranteed by a wide contact area.

Just like the steering axle tyre, the drive axle tyre SmartFlex DH35 has M+S marking and the snowflake symbol. In addition, the tyre also has a wide contact area with four zigzag groove lines over the whole tread surface, enhancing mileage and driving performance under different road and traffic conditions. Furthermore, the 3D sipes ensure high traction and low rolling resistance. The innovative tread sipe design supports low rolling resistance and tyre traction for the drive axle in road traffic. The SmartFlex DH35 is already available in the sizes 215/75R17.5, 235/75R17.5, 245/70R17.5 and 305/70R19.5 with more to follow.

Sizes of the SmartFlex tyre line available

| Tread | Size | LI | Marking |  | M+S | Availability |
| --- | --- | --- | --- | --- | --- | --- |
| AH35 | 8.5R17.5 | 121/120L | D/C/W1 67dB |  |  |  |
|  | 8 R19.5 | 124/122L | D/C/W1 65dB |  |  | In production |
|  | 9.5.R17.5 | 131/129L | D/C/W1 67dB |  |  |  |
|  | 205/75R17.5 | 124/122M | D/C/W1 65dB |  |  |  |
|  | 215/75R17.5. | 126/124M | D/C/W1 65dB |  |  |  |
|  | 225/75R17.5 | 129/127M | C/C/W1 67dB |  |  |  |
|  | 235/75R17.5 | 132/130M | C/C/W1 69dB |  |  |  |
|  | 245/70R17.5 | 136/134M | C/C/W1 69dB |  |  |  |
|  | 245/70R19.5 | 136/134M | C/C/W1 67dB |  |  | In production |
|  | 265/70R17.5 | 140/136M | C/C/W1 65dB |  |  | In production |
|  | 265/70R19.5 | 140/138M | C/C/W1 67dB |  |  |  |
|  | 285/70R19.5 | 146/144M | C/C/W1 67dB |  |  |  |
|  | 305/70R19.5 | 148/145M | C/C/W1 65dB |  |  |  |
| DH 35 | 215/75R17.5 | 126/124M | D/C/W1 66dB |  |  |  |
|  | 205/75R17.5 | 124/122M | C/C/W1 66dB |  |  | In production |
|  | 225/75R17.5 | 129/127M | C/C/W1 73dB |  |  | In production |
|  | 235/75R17.5 | 132/130M | C/C/W1 73dB |  |  |  |
|  | 245/70R17.5 | 136/134M | D/C/W1 73dB |  |  |  |
|  | 8.5R17.5 | 121/120L | D/C/W1 73dB |  |  | In production |
|  | 9.5R17.5 | 131/129L | D/C/W1 73dB |  |  | In production |
|  | 245/70R19.5 | 136/134M | D/C/W1 73dB |  |  | In production |
|  | 265/70R17.5 | 139/136M | D/C/W1 73dB |  |  | In production |
|  | 265/70R19.5 | 140/138M | D/B/W1 73dB |  |  | In production |
|  | 285/70R19.5 | 146/144M | D/B/W1 73dB |  |  | In production |
|  | 305/70R19.5 | 148/145M | D/B/W1 73dB |  |  |  |

Technical properties of the SmartFlex AH35

A Wide contact area:

The wide contact area guarantees high mileage.

B Four wave-shaped and straight grooves:

The combination of four wave-shaped and straight grooves over the whole tread surface on a wide range of different road surfaces guarantees excellent water drainage.

C Multi-3D sipe tread:

The Multi-3D sipe tread offers outstanding traction and thus promotes improved driving stability.

The rigidity of the tread blocks and the resulting minimum block movement lead to significant fuel savings.

D Special tread design with “semi-sipes”:

Special tread design with “semi sipes” guarantees an even wear pattern over the entire service life.

Wide contact area

Multi-3D sipe tread

Technical properties of the SmartFlex DH35

A Wide contact area with 4 zigzag grooves:

The wide contact area and the 4 all-round zigzag tread grooves ensure high mileage and overall performance.

B Multi-3D sipe treads:

The special tread design with Multi-3D sipes promotes low rolling resistance and outstanding traction.

C Innovative tread design:

The special tread design guarantees low rolling resistance and optimum traction under a wide range of different conditions.

Wide contact area

Multi-3D sipe tread

All-rounders for all-year tyres

Particularly in changeable weather conditions, Hankook recommends that truck and bus customers use the SmartFlex all-weather tyre line for medium and long haul trips. Commercial vehicle customers can rely in particular on a high level of driving safety as well as the current trend of increased load-bearing capacity for some sizes.

Hanover/Neu-Isenburg, Germany, 21 September, 2016 – Both the steering axle tyres SmartFlex AH31 and the drive axle tyres SmartFlex DH31 have M+S marking and the snowflake (3PMSF) symbol, which means good traction is guaranteed even if drivers should be surprised by wintry road conditions. The SmartFlex AH31 tyre, winner of the iF Design Award in 2015, has a special tyre profile with decisive safety functions which promotes water drainage in particular and should thus help to prevent potential hydroplaning. The operating costs incurred by fleet operators can also be reduced through the use of the SmartFlex all-season range because irregular wear is avoided on the steering axle thanks to the so-called Tread Wear Equalised Stepper technology used for the SmartFlex AH31, small stabilising blocks on the outside of ribs 2 and 4.

The counterpart for the drive axle is the Hankook SmartFlex DH31. Its 6-rib tread with special hexagonal tread blocks guarantees more even wear behaviour and thus a longer tyre service life. Hankook's patented self-cleaning sipes in the middle of each block prevent damage to the block edges and thus guarantee excellent traction throughout the tyre life.

The SmartFlex all-year tyre line is completed by the corresponding trailer tyre SmartFlex TH31, which is celebrating its premieres at the 66th IAA for Commercial Vehicles. Its wide, closed shoulder area supports stable straight driving and ensures good lateral stability. Chamfered tread grooves help prevent splintering.

Whilst the SmartFlex AH31 and SmartFlex DH31 are designated mainly for larger wheel sizes in the 22.5 inch range, SmartFlex AH35 and its drive axle counterpart SmartFlex DH35 is more designated for smaller wheels with 17.5/19.5 inch sizes.

Sizes of the SmartFlex tyre line available

| Tread | Size | LI | Marking |  | M+S | Availability | Remark |
| --- | --- | --- | --- | --- | --- | --- | --- |
| AH31 | 295/80R22.5 | 152/148M (154M/149L) | C/B/W1 73dB |  |  |  | - |
|  | 295/80R22.5 | 154/149M | C/B/W1 73dB |  |  |  | Tyre with higher load-bearing capacity, mainly for truck use |
|  | 315/80R22.5 | 156/150L | C/B/W1 73dB |  |  |  | - |
|  | 315/70R22.5 | 156/150L | C/B/W1 73dB |  |  |  | - |
|  | 385/65R22.5 | 164K | C/B/W1 69dB |  |  |  | - |
|  | 385/65R22.5 | 160K | C/B/W1 69dB |  |  |  | - |
|  | 315/60R22.5 | 154/148L | C/B/W1 70dB |  |  |  | - |
|  | 385/55R22.5 | 160K | C/B/W1 69dB |  |  |  | - |
| DH31 | 295/80R22.5 | 152/148M | D/C/W2 75dB |  |  |  | - |
|  | 315/80R22.5 | 156/150L | D/C/W2 75dB |  |  |  | - |
|  | 315/70R22.5 | 154/150L | D/C/W2 75dB |  |  |  | - |
|  | 295/60R22.5 | 150/147K | D/C/W2 75dB |  |  |  | - |
|  | 315/60R22.5 | 152/148L | D/C/W2 75dB |  |  |  | - |
| TH31 | 385/65R22.5 | 160K | B/B/W1 69dB | - |  | In production | - |

Technical properties of the Hankook SmartFlex all-year tyre line

SmartFlex AH 31

Truck all-year tyres for the steering axle for medium to long-haul applications

A Extra-wide tread and shoulder area:

- The extra-wide open shoulder area supports a high mileage and traction as well as outstanding handling properties

B Multi-3D sipe treads:

- High traction and mileage with even

wear

C Tread Wear Equalizer Stepper Technology (T.W.E.S.):

- Stabilisers on profile blocks

- Reduction of uneven/one-sided wear

SmartFlex DH 31

Truck all-year tyres for the drive axle for medium to long-haul applications

A Multi-3D sipes:

- High traction and mileage with even wear

B 6-rib block tread:

- Sturdy 6-rib block tread with special hexagonal tread blocks

C Self-cleaning sipes:

- Constant traction over the entire service life

- Protection against splintering at the corners of the sipes

SmartFlex TH 31

Truck all-year tyres for the trailer axle for medium to long-haul applications

A 4 Zigzag sipes:

- 4 main tread grooves ensure optimum water displacement

B Chamfered profile block design:

- Chamfered profile blocks sipes help to prevent material splintering

C Extra-wide tread and shoulder area:

- The extra-wide closed shoulder area supports high driving stability and ensures good lateral stability as well as even wear

###

Hankook AL10+ e-cube MAX:

Low-line sizes for the steering axle

In times when the trend is going more and more towards volume transportation, the legally permissible outside height of four metres for commercial vehicles means that fleet operators are quickly reaching their limits. The issues get amplified if the freight forwarder wants to transport heavy standard goods in addition to volume transports. In this case, the standard sizes 295/60 or 315/60 quickly reach the load capacity limit. Therefore, premium tyre maker Hankook has now released the AL10+ e-cube MAX long distance tyre for the low-line segment. With the dimension of 355/50R22.5, the new low profile tyre for the truck steering axle is designed especially for the requirements of volume transports.

Hanover/Neu-Isenburg, Germany, 21 September, 2016 – Until now, fleet operators with truck tyres of series 60 to 80 have often not been able to completely utilise the maximum inner load height of three metres without exceeding the legally permissible total height of four metres. Therefore, load capacity is lost, which in turn can result in economic disadvantages. As a consequence and following the market trend, premium tyre maker Hankook is offering its customers a truck tyre for the steering axle in series 50: the AL10+ e-cube MAX was developed in size 355/50R22.5 exclusively for use on jumbo trucks for long distances, and it provides a load index of 156, which means that the axle can be loaded with a weight of up to 8 tons. With its smaller diameter, it lowers the coupling height of the tractor engine, with the result that the inner load height increases and the three-metre loading platform can be fully utilised thanks to the lower profile tyres.

The tyre profile e-cube MAX for commercial vehicles represents maximum cost effectiveness, energy efficiency and environmental friendliness: due to its longitudinal grooved tread with wave structure, the AL10+ e-cube MAX for the steering axle prevents uneven wear. Therefore, the tyre guarantees an increased service life. The improved tyre tread and the high load index of the AL10+ e-cube MAX increases the fuel efficiency while offering higher load capacity at the same time. The linear groove structure supports stable directional stability as well as maximum steering precision and improved water dispersal.

The long distance specialist for the steering axle is supported by the DL10+ e-cube MAX for the drive axle. Due to its three-dimensional lamellae, it offers drivers outstanding traction, while the extra-wide profile block and deep grooves ensure increased mileage. The block stabilisers of the DL10+ e-cube MAX also contribute to a high service life and low rolling resistance. The e-cube MAX series is completed by the matching trailer tyre TL10+, which is characterised by maximum driving stability and low rolling resistance.

Sizes of the e-cube MAX tyre line available

| Tread | Size | LI | Marking |  | M+S | Availability |
| --- | --- | --- | --- | --- | --- | --- |
| AL 10+ | 315/80R22.5 | 156/150L (154/150M) | B/B/W1 70dB | - | - |  |
|  | 315/70R22.5 | 156/150L | B/B/W1 70dB | - | - |  |
|  | 385/65R22.5 | 160K | B/B/W1 70dB | - | - |  |
|  | 295/60/R22.5 | 150/147L | C/B/W1 70dB | - | - |  |
|  | 315/60R22.5 | 154/148L | C/B/W1 70dB | - | - |  |
|  | 355/50R22.5 | 156L | C/B/W1 70dB | - | - |  |
| DL 10+ | 315/80R22.5 | 156/150L (154/150 M) | C/C/W1 73dB |  |  |  |
|  | 315/70R22.5 | 154/150L | C/C/W1 73dB |  |  |  |
|  | 295/60R22.5 | 150/147K | C/C/W1 73dB |  |  |  |
|  | 315/60R22.5 | 152/148L | C/C/W1 73dB |  |  |  |
|  | 295/55R22.5 | 147/145K | C/C/W1 73dB |  |  | In production |
|  | 315/45R22.5 | 147/145L | D/C/W2 75dB |  |  | In production |
| TL10+ | 215/75R22.5 | 135/133J | C/B/W1 71dB | - | - |  |
|  | 235/75R22.5 | 143/141J | B/B/W1 69dB | - | - |  |
|  | 245/70R17.5 | 143/141J (146/146F) | B/B/W1 69dB | - | - |  |
|  | 265/70R19.5 | 143/141J | B/B/W1 69dB | - | - |  |
|  | 385/55R22.5 | 160K(158L) | B/B/W1 70 dB | - | - |  |
|  | 385/65R22.5 | 160K | B/B/W1 69 dB | - | - |  |
|  | 435/50R19.5 | 160J | B/B/W2 73 dB | - | - |  |
|  | 455/40R22.5 | 160J | B/B/W2 71 dB | - | - |  |

Technical properties of the e-cube MAX range

1. Optimised tread compound

- “Low hysteresis” tread compound reduces rolling resistance:

High molecular weight rubbers with very long-chain molecules, which have a lower tendency of branching and thus fewer free chain ends, are processed at reduced temperatures and extended mixing periods in Hankook's innovative mixture process IMS (Innovative Mixing System). This results in a significant increase in the connection rate between the carbon black and rubber molecules and a much more consistent distribution within the mixture.

- Reduction of the loss of energy caused by heat development.

2.Stiffness Control Contour Theory (SCCT)

- Patented Hankook design technology for the even distribution of pressure inside the tyre and increased stability as well as movement in the tyre.

- High carcass durability and economy, improved retreadability.

Hankook SmartControl AW02: Winter tyres developed for truck steering axles and all other tyre positions

The SmartControl AW02 is Hankook's winter specialist for trucks that can be used on the steering axle and all other positions. Like all the other treads in the SmartControl tyre line, the tyre, which is suitable for use on all axles, not only impresses with the M+S marking but also with the "Three Peak Mountain Snowflake" (3PMSF) symbol, which verifies its high winter performance.

Hanover/Neu-Isenburg, Germany, 21 September, 2016 - The SmartControl AW02 and the SmartControl DW07 for the drive axle are part of Hankook's successful range of winter tyres for trucks which is being completed at the 66th IAA for Commercial Vehicles through the presentation of the trailer tyre SmartControl TW01.

The tyre tread of the SmartControl AW02 is designed entirely with safety in mind. Hankook's winter specialist for trucks has an extra wide tread which increases the contact area between the tyre and the road thereby improving handling. In addition, the tread design with five main drainage grooves enhances water displacement. Furthermore, 3D sipes in the tread surface fulfil two important tasks: On the one hand they ensure even tread wear and thus guarantee high mileage. On the other, in combination with the unique half-open shoulder design of the SmartControl AW02, they provide for outstanding tyre traction on ice- and snow-covered roads. The individual blocks are also connected with ridges that have a stabilising effect for even better handling properties and continuous high performance quality.

Thanks to the tyre compound especially designed for harsh winter conditions, the tyre is particularly cold-resistant and demonstrates full performance even at very low temperatures. At the same time, the special compound of the SmartControl AW02 achieves high mileage with a reduction of fuel consumption.

Sizes of the SmartControl AW02 available

| Tread l | Size | LI | Marking |  | M+S | Availability |
| --- | --- | --- | --- | --- | --- | --- |
| AW02 | 295/80R22.5 | 154/149M | D/C/W1 70dB | ( | ( | ( |
|  | 315/80R22.5 | 156/150L | D/C/W1 70dB | ( | ( | ( |
|  | 275/70R22.5 | 150/145J | D/C/W1 70dB | ( | ( | In production |
|  | 315/70R22.5 | 154/150L | D/C/W1 70dB | ( | ( | ( |
|  | 385/65R22.5 | 160K | C/C/W1 70dB | ( | ( | ( |
|  | 385/55R22.5 | 160K | C/C/W1 70dB | ( | ( | ( |

Technical properties of the SmartControl AW02

1. Extra-wide tread and five grooves in zigzag design

- Larger contact area

- Outstanding handling

- Excellent water drainage

2. 3D sipes, bars between the blocks and half-open shoulder design

- Even tread wear

- High mileage

- Perfect traction and handling properties

3. Innovative rubber compound

- The tread compound is tuned particularly to wintry conditions and promotes a consistent performance and low rolling resistance even at cold temperatures.

###

Hankook SmartControl DW07:

Winter specialist for the drive axle

The SmartControl DW07 is Hankook's winter specialist for truck drive axles. The “Snowflake” (3PMSF) symbol attests the winter performance of the SmartControl DW07 on snow- and ice-covered roads. Compared with predecessor models, the tyre offers up to 25% more traction on snow and up to 13% more mileage on wintry roads.

Hanover/Neu-Isenburg, Germany, 21 September, 2016 – The Hankook SmartControl DW07 was developed with use under extreme wintry conditions in European long-haul and delivery traffic in mind. It is part of the SmartControl tyre line, which also includes the SmartControl AW02 for the steering axle and the SmartControl TW01 for trailers.

Drivers and fleets must be equipped to face the toughest of wintry conditions in order to avoid expensive downtimes and arrive safely at their destination. Thus optimum snow traction is a central requirement on winter tyres on the drive axle in transport and delivery traffic, alongside high mileage. The special tread design and the tread compound for the SmartControl DW07 developed for winter use have been optimised particularly for journeys in regions with extremely demanding wintry conditions such as those which occur in northern Europe and the Alps.

The tyre tread of the SmartControl DW07 has been designed especially for snow performance and safety on wintry roads. The tread of Hankook's truck winter specialist for the drive axle is 8% wider than its predecessor model, increasing the contact area between tyre and surface and thus improving grip and handling. In addition, the tread design with five main drainage grooves improves hydroplaning safety. 3D  sipes which are very close together in the tread fulfil two important tasks at the same time: on the one hand they ensure more even tread wear and thus guarantee a high mileage. On the other, in combination with the half-open shoulder design of the SmartControl DW07, they produce improved tyre traction on ice- and snow-covered roads. The serrated edges of the tyre tread blocks also support braking and traction performance thanks to optimum tyre grip on wintry surfaces.

Innovative technologies make the SmartControl DW07 particularly efficient. A specially developed tyre compound is used for Hankook's truck winter specialist, which has been optimised for tough wintry conditions and remains flexible even at cold temperatures. The tyre is particularly cold-resistant and has a high braking performance even at very low temperatures. At the same time, the arrangement of the tread blocks has been designed particularly with shock absorption in mind, making even wear and thus a high mileage possible.

Sizes of the SmartControl DW07 available

| Tread | Size | LI | Marking |  | M+S | Availability |
| --- | --- | --- | --- | --- | --- | --- |
| DW07 | 12R22.5 | 152/148L | D/C/W1 72dB | ( | ( | ( |
|  | 275/70R22.5 | 148/145J | D/C/W1 72dB | ( | ( | In production |
|  | 295/80R22.5 | 152/148L | D/C/W1 69dB | ( | ( | ( |
|  | 315/70R22.5 | 154/150L | D/C/W1 71dB | ( | ( | ( |
|  | 315/80R22.5 | 156/150L | D/C/W1 72dB | ( | ( | ( |

Technical properties of the SmartControl DW07

- Pentagonal block design for optimum grip on snow and ice

- Enlarged pentagonal blocks enable the load to be spread over the whole contact area for optimum winter performance.

- The serrated edges of the tread blocks make optimum grip on wintry surfaces possible for high braking and traction performances.

- 3D sipe technology for driving stability and maximised traction on snow

- Significantly larger number of 3D sipes for high snow trip and traction over the whole service life.

- Half-open shoulder design for improved traction and cornering on ice- and snow-covered roads.

- Extra-wide tread design for optimised driving stability

- Wider shoulder blocks (+8% compared to the predecessor model) increase mileage by up to 13%.

- Optimised block design for high traction.

###

Hankook SmartControl TW01:

New winter specialist for trailer tyres

Premium tyre maker Hankook present a new specialist winter tyre for truck trailers: the SmartControl TW01. Alongside the existing steering and drive axle tyres of the series, Hankook will now offer customers a complete winter solution. The SmartControl TW01 is available in size 385/65R22.5, with more sizes to follow. Hankook will exhibit the new tyre at the 66th IAA Show for Commercial Vehicles in Hanover this year.

Hanover/Neu-Isenburg, Germany, 21 September, 2016 – For the first time, premium tyre maker Hankook present a winter tyre specifically for trailer axles. The SmartControl TW01 complements Hankook’s SmartControl winter tyre line, which already includes the SmartControl AW02 for steering axles and the SmartControl DW07 for drive axles. Like both of these tyres, the new SmartControl TW01 has the M+S marking and the “Three Peak Mountain Snowflake” (3PMSF) symbol. This makes it particularly well suited for driving in the most extreme winter conditions.

The inner three ribs of the 5-rib tread on this new winter specialist are equipped with Multi-3D sipes which guarantee excellent braking performance on wet, snow and ice covered roads. They also provide the tread blocks with a high degree of stability which results in uniform tread wear and high mileage and fuel efficiency. The four main tread grooves, which are designed in a zigzag pattern, provide excellent lateral stability. In addition, they ensure optimal water displacement which reduces the risk of aquaplaning on wet or slushy roads. Solid, sipeless shoulder blocks on both outer tread ribs of the SmartControl TW01 provide stability and excellent grip on both wet and dry roads as well as high mileage performance.

The rubber compounds of the SmartControl TW01 are specifically designed for wintry conditions. The addition of a particularly cold-resistant (low Tg) synthetic rubber material ensures that the tread compound does not harden, even in extremely low outdoor temperatures, and thus retains good winter characteristics at all times. The special tread compound has a favourable impact on mileage performance and rolling resistance.

Due to the special structure in the composition of the Smart Control line, belt movements can be reduced to a minimum, resulting in overall cooler-running tyre temperatures and therefore greater fuel-efficiency. In addition, Hankook’s SCCT (Stiffness Control Contour Theory) technology guarantees an optimised contour for good handling, and the advanced bead wire tread contributes to excellent retreadability. The expansion of the SmartControl series, including new sizes for steering and drive axles, is planned for the coming year.

Sizes of the SmartControl tyre line available

| Tread | Size | LI | Marking |  | M+S | Availability |
| --- | --- | --- | --- | --- | --- | --- |
| TW01 | 385/65R22.5 | 160K (158L) | B/C/W1 69dB |  |  | In production |

Technical properties of the SmartControl TW01

1. Zigzag grooves

- Four zigzag tread grooves guarantee excellent lateral guidance and ensure optimum water drainage.

2. Multi-3D sipe treads

- The Multi-3D sipe tread ensures an outstanding braking performance.

- The stability of the tread blocks and the resulting minimum block movement lead to significant fuel savings.

3. Wide shoulders

- The wide shoulders ensure excellent wet grip and high driving stability.

4. Innovative rubber compound

- The tread compound is tuned particularly to wintry conditions and promotes a consistent performance and low rolling resistance even at cold temperatures.

###

Hankook SmartWork: Sturdy and durable for on and off-road

Hankook's truck range for use on construction sites, comprising of the tyres SmartWork AM09, SmartWork AM15/AM15+ for the steering axle, the SmartWork DM09 for the drive axle and the SmartWork TM15 for the trailer, was developed especially for the demanding tasks in the on- and off-road segment. All the tyres have been designed for heavy weights and high loads, and stand out on account of their high resistance to splintering, cuts and tread breaks. Other convincing features include their self-cleaning function and an extremely sturdy carcass structure.

Hanover/Neu-Isenburg, Germany, 21 September, 2016 – The SmartWork AM09 for the steering axle is suitable for construction site vehicles which are more frequently used on roads. Its polygonal tread blocks ensure excellent traction and outstanding braking performance even on muddy roads. Both the extra-wide tread design and the closed shoulder area provide the SmartWork AM09 with a high degree of driving stability. Special rubber blocks in the profile grooves prevent stones from becoming lodged. The SmartWork AM15/AM15+ is also suitable for the steering axle, but has been designed especially for off-road use. Its extra-wide tread blocks guarantee optimum traction on uneven surfaces like those typical of construction sites. Its open shoulder area with tie-bar also contributes to this. Extra-wide tread grooves prevent gravel becoming lodged in the tread.

The SmartWork DM09 is available for the drive axle. The directional tread design enables improved displacement of mud and water. The interblock tie-bar at the centre of the SmartWork DM09 guarantees outstanding straight driving performance and impact dispersion for blocks, thereby improving longevity. Chamfered tread blocks on the outside of the tread surface increase resistance to lateral strains and effectively help prevent damage to the tyre's shoulder or tearing of the block edges.

The trailer tyre SmartWork TM15 included in the line has particularly high traction thanks to its high groove width. In addition, the trailer tyre stands out on account of very good water repulsion. Thanks to their M+S marking, all the treads of the SmartWork series can be utilised on and off-road all year round even in wintry conditions.

As with other tyre ranges from Hankook, the SmartWork line also features the Hankook SCCT technology (Stiffness Control Contour Theory): this enables the particularly even distribution of the tyre pressure even under heavy loads. This way the deformation strain that affects the carcass is minimised. This not only positively influences the longevity of the tyre but also performance features like braking characteristics and the retreadability of the tyres.

Sizes of the SmartWork line available

| Tread | Size | LI | Marking |  | M+S | Availability |
| --- | --- | --- | --- | --- | --- | --- |
| AM09 | 10R22.5 | 144/142K | C/B/W1 70dB | - | ( | ( |
|  | 11R22.5 | 148/145K | D/B/W1 67dB | - | ( | ( |
|  | 13R22.5 | 156/150K | D/C/W1 70dB | - | ( | ( |
|  | 295/80R22.5 | 152/148K (154/150J) | C/B/W1 67dB | - | ( | ( |
|  | 315/80R22.5 | 156/150K | D/B/W1 67dB | - | ( | ( |
| DM09 | 13R22.5 | 156/150K | D/C/W2 75dB | - | ( | ( |
|  | 1200R20 | 154/150K | E/C/W2 75dB | - | ( | ( |
|  | 295/80R22.5 | 152/148K | E/B/W1 70dB | - | ( | ( |
|  | 315/80R22.5 | 156/150K | D/C/W1 70dB | - | ( | ( |
| AM15 | 265/70R19.5 | 143/141J | D/B/W2 74dB | - | ( | ( |
|  | 275/70R22.5 | 148/145K | D/B/W2 74dB | - | ( | ( |
|  | 385/65R22.5 | 160K/(158L) | D/C/W2 74dB | - | ( | ( |
|  | 425/65R22.5 | 165K | C/C/W2 75dB | - | ( | ( |
|  | 445/65R22.5 | 169K | C/C/W2 75dB | - | ( | ( |
| AM15+ | 385/65R22.5 | 160K/(158L) | D/C/W2 74dB | - | ( | ( |
| TM15 | 385/65R22.5 | 160K/158L | D/C/W1 69dB | - | ( | ( |

Technical properties of the Hankook SmartWork AM09

- Wider zigzag grooves for high traction and optimised braking performance:

- Four extra-wide tread grooves in a zigzag design guarantee the right grip both on tarmac roads and off-road.

- Excellent displacement of mud and water.

- Additional pimples in the grooves support the tyre's self-cleaning function.

- Polygonal, stepped blocks for a more pronounced edge effect:

- Special notches on the individual tread blocks for particularly good grip.

- Shorten braking distance.

- Enhance off-road traction.

- Closed shoulder design increases the tyre's driving stability:

- Improved resistance against forces acting at the side.

- Protection against damage to the block edges.

- Shoulder lugs help to produce less heat while driving.

Technical properties of the Hankook SmartWork AM15/AM15+

- Optimised tread blocks

- Bars between the tread blocks stabilise the tyre.

- The optimised contact area prevents uneven wear.

- Particularly wide and deep grooves for better traction and to prevent stone damage

- Grooves ideally displace water and guarantee an extremely high mileage.

- Ribs within the grooves prevent stones becoming lodged in the tread.

- Innovative rubber compound reduces heat development

- Specially developed mixing method slows wear and increases mileage.

- Retreading is made easier and the tyre can be used again more quickly.

Technical properties of the Hankook SmartWork DM09

1.	Hankook SCCT technology (Stiffness Control Contour Theory):

-	The particularly even distribution of tyre pressure even under heavy loads effectively minimises the deformation load acting on the carcass, resulting in optimal retreadability, cornering and braking characteristics, short braking distances as well a generally high durability.

2.	Optimised tyre tread:

-	Block design with reinforced central rib for more even distribution of the forces acting in use.

-	More uniform abrasion pattern and minimisation of uneven wear.

- 	High grip on loose surfaces and very good self-cleaning properties thanks to the open tyre shoulder design.

- 	Conical tread blocks on the outer side of the tread for increased resistance to side loads and protection of the block edges in the shoulder area.

3.	Hankook Innovative Mixing System:

-	Especially even distribution of the carbon black particles and rubber molecules within the compounds thanks to longer mixing times at reduced temperatures.

- 	The significantly increased bonding rate between the carbon black and rubber molecules results in lower heat development during driving for less rolling resistance and fuel consumption.

Technical properties of the Hankook SmartWork TM15

Optimised tyre tread:

- Wider tread grooves compared to the predecessor model ensure improved traction

- Sipes in the centre of the three tread grooves prevent stones becoming lodged in the tread

- Bars between the tread blocks increase their rigidity, thus promoting more even wear

###

Hankook TH22: Trailer tyres for low-bed truck transport

The TH22 is Hankook's trailer specialist when it comes to transporting heavy loads in regional traffic, along country roads for example. Because alongside the standard sizes, the TH22 is available in smaller sizes which can then be fitted to low-bed trucks, making maximum loading volume possible.

Hanover/Neu-Isenburg, Germany, 21 September, 2016– The Hankook TH22 is the successful trailer tyre from the premium tyre maker for regional and shuttle traffic, which was launched in 2011. The TH22 is available in standard sizes 235/75R17.5, 245/70R17.5 and 265/70R19.5 and also in smaller sizes especially for use on low-bed trailers.

The profile and carcass design of the Hankook TH22 trailer tyre optimises wear resistance as well as rolling resistance. The closed 4-rib block profile with extra-broad, solid shoulder ribs was especially developed for low rolling resistance and good lateral stability. At the same time, the tread design supports even wear and 10 percent higher mileage than its predecessor. Wave-shaped tread sipes and transverse sipes right down to the base of the groove additionally provide for effective water displacement, making the TH22 a true all-round talent when it comes to handling.

With the TH22 Hankook is also relying on the patented IMS solution (Innovative Mixing System), which is already being used in many truck tyre ranges in the premium tyre maker's portfolio. Rubbers with particularly long-chain molecules are used for production. This results in significantly cooler operation and significantly increased mileage.

The low design height ensures maximum loading volume and, coupled with the high load-bearing capacity, makes the Hankook TH22 in the sizes 205/65R17.5 and 215/75R17.5 particularly suitable for low-bed trailer heavy-duty transport on country roads, such as car, construction vehicle or construction element transport.

Available sizes of the TH22

| Tread | Size | LI | Marking |  | M+S | Availability |
| --- | --- | --- | --- | --- | --- | --- |
| TH22 | 9.5R17.5 | 143/141J | D/B/W1 70dB | - |  |  |
|  | 11R22.5 | 148/146L | C/B/W1 70dB | - |  |  |
|  | 215/75R17.5 | 135/133J | D/B/W1 70dB | - |  |  |
|  | 235/75R17.5 | 143/141J | C/B/W1 70dB | - |  |  |
|  | 245/70R17.5 | 143/141J (146/146F) | C/B/W1 70dB | - |  |  |
|  | 245/70R19.5 | 141/140J | C/B/W1 67dB | - |  |  |
|  | 265/70R19.5 | 143/141J | C/B/W1 70dB | - |  |  |
|  | 285/70R19.5 | 150/148J | C/B/W1 70dB | - |  |  |
|  | 205/65R17.5 | 129/127J |  | - |  | In production |
|  | 385/65R22.5 | 164K (160K) | C/B/W1 70dB | - |  |  |
|  | 425/65R22.5 | 165K | B/B/W1 71dB | - |  |  |
|  | 385/55R22.5 | 160K (158L) | B/B/W1 71dB | - |  |  |

Technical properties of the Hankook TH22

1.	Tyre design

- 	Belt structure: Less belt deformation guarantees very low rolling resistance

-	Carcass structure: The wider carcass profile with reinforced

belt cord guarantees  excellent durability

- 	Bead structure: Reinforced bead structure ensures a long service life even at high load weights

2.	Tread design

-	Optimised zigzag rib design for good self-cleaning

-	Wide and firm shoulder package for improved mileage and even wear

-	Solid, continuous centre rib improves rolling characteristics and lateral stability

###

About Hankook

Hankook Tire is one of the global top 5 companies in the mass production of tyres and manufactures innovative, award winning radial tyres of proven superior quality for passenger cars, light trucks, SUVs, RVs, trucks and buses as well as motorsports (circuit racing/rallies). Hankook continues to invest in research and development so that we can always offer our customers the highest level of quality, combined with technological excellence. At a total of five development centers and seven large scale factories around the world, the company develops and produces tyre solutions specially tailored to the requirements and needs of regional markets. Bespoke tyre solutions for the European markets as well as European Original Equipment according to the requirements of leading premium car manufacturers, are developed in the company’s regional Technical Centre in Hanover/Germany. Production for the European region is taking place in the state-of-the-art manufacturing site in Rácalmás/Hungary which was inaugurated in June 2007 and is continuously being expanded. Currently more than 3,000 employees produce up to 19 million tyres a year for passenger cars, SUVs and light trucks.

Hankook Tire’s European headquarters are located in Neu-Isenburg near Frankfurt am Main in Germany. The manufacturer operates further branches in Germany, UK, France, Italy, Spain, the Netherlands, Hungary, Czech Republic, Russia, Turkey, Sweden and Poland. Hankook products are sold directly through regional distributors in other local markets. Hankook Tire employs more than 22,000 people worldwide and are selling their products in over 180 countries. Internationally leading car manufacturers rely on tyres made by Hankook for their original equipment. Approximately 30 percent of the company's global sales are generated within the European and CIS-Region.

For more information please visit www.hankooktire-mediacenter.com

Media contact:

Hankook Tire Europe GmbH | Corporate Communications Europe/CIS

Siemensstr. 5a, 63263 Neu-Isenburg | Germany

Felix Kinzer, Director

Corporate and Finance Communications, Technologies, R&D/Production Operations

Tel.: +49 (0) 61 02 8149 – 170

Mobile: +49 160 97774983

f.kinzer@hankookreifen.de

Anna Pasternak, PR Manager

LT and Truck & Bus Tyres, Intl. Motorsports, CSR

Tel.: +49 (0) 6102 8149 – 173

Mobile: +49 151 65641014

a.pasternak@hankookreifen.de

Sabine Riedel, Public Relations

LT and Truck & Bus Tyres, Hankook Media Center, SNS, Corporate

Tel.: +49 (0) 6102 8149 – 174

Mobile: +49 160  2545318

s.riedel@hankookreifen.de

Larissa Büsch, Public Relations

PCR/ SUV, Event

Tel.: +49 (0) 6102 8149 – 171

Mobile: +49 160 2252301

l.buesch@hankookreifen.de

Yara Willems, Public Relations Assistant

Corporate, SNS

Tel.: +49 (0) 6102 8149 – 172

Mobile: +49 160 2545279

y.willems@hankookreifen.de

# Text boxes

- The tyre provides up to eight percent improved tyre related fuel efficiency.

- 55 percent more durability in comparison to conventional products, e.g. through a significant reduction of uneven tyre wear.

- More mileage thanks to new developed tread  compound

A: Reinforced tread blocks:

- Interlocking central rib tread blocks for low rolling resistance.

# B: Shoulder block design:

# - The largely closed tread design in the shoulder rib area ensures particularly uniform tyre wear.

C: Sipes design:

- 3D full deep kerfs guarantee outstanding braking response throughout the life of the tyre.

A: Block Design:

- Central 4-block design of the massive central rib for high traction combined with reduced rolling resistance.

B: Joining ridges:

# - Tie bars in the open shoulder block area for more traction and reduction of uneven wear.

C: Sipes design:

- 3D full deep kerfs guarantee outstanding braking response throughout the life of the tyre.

# .

A: Tyre contour:

- Extra wide tread area for very high driving stability and improved wear resistance.

B: Multi sipes:

- Multi-sipes added in the central rib area prevent uneven wear without affecting tread rib stability

In 2015 the SmartControl AW02 received the Red Dot Design Award.